## Slide 1
MAI605 · Robotic Systems (ROS2)
Industrial
Pick · Scan · Place
Robot Cell
A fully integrated ROS 2 manipulation pipeline combining
MoveIt 2 planning · QR perception · autonomous sorting
Maryam Ali | ID 202512707
Maitha Alghfeli | ID 202512976
Instructor: Prof. Omar Osama Shalash
Date: 30 April - 2026
ROS 2
MoveIt 2
Gazebo
zbar_ros
KDL IK
OMPL
MAI605 Course Project I — ROS 2

## Slide 2
Project Description & Objectives
what the system does and why it was built
WHAT THE SYSTEM DOES
A simulated 6-DOF robot arm picks a QR-tagged object from a fixed station, lifts it to a safe height, carries it to a scan station, decodes the QR code, and places the object into the correct sorting bin — then returns home and repeats.
TECH STACK
MoveIt 2
motion planning & trajectory execution
Gazebo Classic
physics simulation & world environment
ros2_control
100 Hz joint trajectory controllers
zbar_ros
real-time QR code decoding
State Machine
coordinator orchestrates all 10 stages
PROJECT OBJECTIVES
01
Implement a fully integrated ROS 2 manipulation system with at least 5 DOF combining perception, planning, and control.
02
Build a URDF/Xacro robot model and configure the MoveIt 2 planning environment with named states and collision geometry.
03
Develop collision-free trajectories for approach, grasp, lift, scan, and placement motions using OMPL planners.
04
Integrate QR perception via zbar_ros and route decoded payloads to the correct destination bin.
05
Design a modular ROS 2 architecture — clean nodes, topics, services, parameters, and launch files.
06
Demonstrate end-to-end system performance through Gazebo simulation with full documented evidence.

## Slide 3
What We Built
An end-to-end autonomous sorting cell — from steel fixture to sorted bin
6-DOF Robot Arm
Custom URDF/Xacro model with 6 revolute joints, 1 prismatic gripper, and a wrist-mounted camera frame. Fully integrated with ros2_control at 100 Hz.
QR Perception
zbar_ros decodes QR-tagged objects at the scan station. A custom bridge normalizes and deduplicates the payload before publishing to downstream nodes.
Autonomous Sorting
A coordinator state machine drives 10 discrete stages — pick, lift, scan, decide, place, return — with layered fallback strategies at every step.
8 ROS 2 Packages
10 Workflow States
7 Controllable Joints
3 Sorting Bins

## Slide 4
System Architecture
Eight ROS 2 packages, one clean data pipeline
robot_description
URDF · kinematics · collision geometry
moveit_config
SRDF · planners · KDL IK · controllers
workflow_interfaces
BinTarget.msg · ExecuteStage.srv
manipulation
Stage execution · planning scene
perception
QR stream · zbar_ros · normalization
decision_logic
QR → bin routing · pose publication
simulation
Gazebo world · attachment helper
bringup
Full-stack launch · coordinator
DATA FLOW
Camera
→ QR
→ Bin
→ Arm

## Slide 5
Robot Mechanical Design
6-DOF serial manipulator with simplified 1-DOF gripper
JOINT CONFIGURATION
shoulder_pan
Revolute
±180°
shoulder_lift
Revolute
−103°/+92°
elbow
Revolute
±120°
wrist_pitch
Revolute
±138°
wrist_yaw
Revolute
±180°
wrist_roll
Revolute
±180°
gripper
Prismatic
0–40 mm
Chain length (nominal)
1.28 m
Total DOF (arm)
6 revolute
Gripper DOF
1 prismatic
Base mass
18.0 kg
Arm total mass
≈ 35 kg
Controller rate
100 Hz

## Slide 6
End-to-End Workflow
Coordinator state machine — 10 stages, one repeatable cycle
IDLE
▶
MOVE TO PICK
▶
GRASP
▶
LIFT
▶
MOVE TO SCAN
▼
RETURN HOME
◀
RELEASE
◀
MOVE TO PLACE
◀
DECIDE BIN
◀
WAIT FOR QR
↺ loops back to IDLE

## Slide 7
Motion Planning & Kinematics
MoveIt 2 with OMPL · KDL numerical IK · multi-layer fallback
FORWARD KINEMATICS
T_world_tool0(q) =
Tz(0.80) · Rz(q₁) ← base lift + yaw
· Tx(0.08) · Ry(q₂) ← shoulder
· Tx(0.36) · Ry(q₃) ← elbow
· Tx(0.32) · Ry(q₄) ← wrist pitch
· Tx(0.16) · Rz(q₅) ← wrist yaw
· Tx(0.12) · Rx(q₆) ← wrist roll
· Tx(0.24) ← tool offset
INVERSE KINEMATICS · KDL Solver
Plugin
KDLKinematicsPlugin
Resolution
0.005 rad
Timeout
0.1 s per attempt
Attempts
3 (then fallback)
MULTI-LAYER FALLBACK STRATEGY
1st
Named SRDF joint state (no IK needed)
2nd
Full 6D pose target — setPoseTarget()
3rd
Position-only — setPositionTarget()
4th
Cartesian path — computeCartesianPath()
5th
Safe fallback posture (accepted on timeout)

## Slide 8
Perception & Decision Logic
From pixel to bin — QR decoding and routing in three steps
Scan-Station
Camera
/scan_station_camera/image_raw
→
zbar_ros
Decoder
/barcode → raw text
→
Bridge Node
Normalizer
/perception/decoded_qr
→
Decision
Logic Node
/decision_logic/bin_target
DEFAULT QR ROUTING MAP
RED
→ bin_a
(0.62, 0.55, 1.18)
BLUE
→ bin_b
(0.82, 0.55, 1.18)
GREEN
→ bin_c
(1.02, 0.55, 1.18)

## Slide 9
ROS 2 Infrastructure
Topics · Services · Actions — the communication backbone
TOPICS (Pub/Sub)
/barcode → std_msgs/String
/perception/decoded_qr
/decision_logic/bin_target
/coordinator/state
/manipulation/status
/demo_qr/image_raw
/scan_station_camera/image_raw
/wrist_camera/image_raw
SERVICES (Req/Resp)
/manipulation/execute_stage
→ ExecuteStage.srv
/simulation/set_attachment
→ std_srvs/SetBool
/simulation/reset_object
→ std_srvs/Trigger
/coordinator/start_cycle
→ std_srvs/Trigger
ACTIONS (Goal/Result)
/arm_controller/
follow_joint_trajectory
/gripper_controller/
follow_joint_trajectory
JointTrajectoryController
@ 100 Hz update rate

## Slide 10
Gazebo Simulation Environment
A compact sorting cell — pick table · scan pedestal · bin rack
ROBOT
BASE
PICK TABLE
(0.72, 0.00)
QR OBJ
SCAN
PEDESTAL
(0.40, −0.48)
BIN RACK (0.82, 0.55)
Bin A
Bin B
Bin C
↑ Schematic top-down layout (not to scale)
WORLD POSES
Pick table
(0.72, 0.00, 0)
z_top = 0.75 m
Scan pedestal
(0.40, −0.48, 0)
—
Bin rack
(0.82, 0.55, 0)
—
Bin A
(0.62, 0.55, 0.75)
RED payload
Bin B
(0.82, 0.55, 0.75)
BLUE payload
Bin C
(1.02, 0.55, 0.75)
GREEN payload
QR object
(0.72, 0.00, 0.825)
gravity off

## Slide 11
Challenges & Limitations
Engineering trade-offs made to focus on system integration and workflow validation
No online localization
All pick and placement positions are pre-measured. The system cannot adapt if the object or bin moves.
Simulated grasping only
Object follows tool0 via TF — no contact physics, no force feedback, no grasp quality check.
No force / tactile sensing
Grasp failures are invisible. A missed pick cannot be detected or recovered automatically.
Numerical IK — no closed-form
KDL may fail near singularities or joint limits. Convergence is not guaranteed.
Static planning scene
MoveIt is unaware of any obstacle not placed at startup. No dynamic obstacle handling.
Idealized QR perception
Default mode uses a synthetic image. Real cameras introduce blur, lighting noise, and partial occlusion.
These are deliberate trade-offs for a teaching platform — not bugs. Each one defines a clear path for the next iteration.

## Slide 12
Recommended Future Improvements
Each limitation maps directly to a concrete next step — no architectural redesign needed
Perception-based
pose estimation
Depth camera / point cloud → remove fixed pick positions
Contact-aware
grasping
Gazebo grasp plugin → real force & slip detection
Analytical
IK solver
Closed-form IK → eliminate KDL timeout & singularity failures
Dynamic obstacle
handling
Runtime scene updates from sensors → moving obstacles
Coordinator
fault recovery
Retry & recovery policies → no manual restart on failure
Planning scene
fidelity
Align MoveIt geometry to Gazebo within centimetres
Cycle performance
logging
Planning time · success rate · execution time per stage
Conveyor &
multi-object support
Moving conveyor + object sequences → real industrial throughput
The clean package separation means each module can be upgraded independently — no full redesign required.

## Slide 13
System Demo — What You Will See
A complete autonomous cycle running in Gazebo Classic + RViz
01
System Launch
bringup launches Gazebo, RViz, MoveIt, controllers, perception, and coordinator in one command.
02
Pick Phase
Arm moves to pre_grasp, descends to the fixture, closes gripper, attaches the QR object, and lifts clear.
03
Scan Phase
Robot carries the object through transit to the scan station. zbar_ros decodes the QR payload in real time.
04
Sort & Place
Decision node maps the payload to a bin pose. Arm rises, translates above the bin via Cartesian path, and releases.
05
Return Home
Robot retreats through staged fallbacks to the home configuration. Coordinator resets and the cycle repeats.
✓ System Functionality 35% ✓ ROS 2 Architecture 20% ✓ Motion Planning 15% ✓ QR Scanning 10% ✓ Code Quality 10% ✓ Report 10%

## Slide 14
Thank You
Any Questions !
What this project demonstrates:
Full URDF/Xacro modelling with ros2_control
Clean ROS 2 topic / service / action architecture
MoveIt 2 planning with multi-layer IK fallbacks
zbar_ros QR pipeline driving autonomous decisions
State-machine coordinator orchestrating all stages
Full simulation in Gazebo + RViz visualization
MAI605 · Robotic Systems (ROS2) · Robotics